## Slide 1: April 2018 ICT 5307 : Embedded System Design
Lecture 2
Input/Output of Digital Data
S.M. Lutful Kabir
Professor, IICT, BUET

## Slide 2: Ports of AVR ATmega32
Port A
Port B
Port D
Port C

## Slide 3: ATMega32 Pin out & Descriptions

## Slide 4: ATMega32 Pin out & Descriptions

## Slide 5: DDRx Register Role in Outputting Data
Each of the Ports A-D in ATmega32 can be used for Input or Output.
DDRx I/O register is used solely for the purpose of making a given port input or output port.
For example, to make a port an output, we write 1s to the DDRx register.
In other words, to output data to all of the pins of Port B, we must first put 0b11111111 (0xFF) into DDRB register to make all the pins output.

## Slide 6: How data is sent to the output port?
Once you set the direction of a port as output, the data that you want to send to the output, you have to write that data into PORTx register.
If DDRC=0xFF and then PORTC=0x3B, the data at the output will also be 0x3B.
That is -
0
0
1
1
1
0
1
1
PC7
PC6
PC5
PC4
PC3
PC2
PC1
PC0

## Slide 7: A Practical example of Outputting Data through a Port
Let us assume that 8 LEDs are connected to 8-pins of PORTC of an Atmega32 chip
We want to glow all of the eight LEDs.
And they will be switched off after1 sec and it will be repeated continuously.
Write a C code for the above mentioned output operations.

## Slide 8: Connection of LEDs with a Port
PC7
PC6
PC5
PC4
PC3
PC2
PC1
PC0
R
GND
ATmega32

## Slide 9: All LEDs glow and off at an interval of 1 sec. And the process is repeated.
PORTC=0xFF
while (1)
{
PORTC=~PORTC;
delay_ms(1000);
}
}
1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
0xFF
0x00

## Slide 10: Alternate LEDs will glow and toggle at every 1 sec
PORTC=0xAA
while (1)
{
PORTC=~PORTC;
delay_ms(1000);
}
}
1 | 0 | 1 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 1 | 0 | 1
0xAA
0x55

## Slide 11: 7-segment display: Introduction
Seven segment displays are very common for electronic product to display numerical output.
Many common devices like calculators, lift, watches, electronic weighing scales, ovens etc use them.
A seven-segment display is so named because it is divided into seven different segments that can be switched on or off.
It can display digits from 0 to 9 and quite a few characters like A, b, C, ., H, E, e, F, n, o, t, u, y, etc.
Knowledge about how to interface a seven segment display to a micro controller is very essential in designing embedded systems.

## Slide 12: The Pin Out and Picture of a 7-segment Display
a
b
d
e
g
b
c
f
g
b
c
g
e
d
2 4 d

## Slide 13: Two types of 7-segment display
Seven segment displays are of two types, common cathode and common anode.
In common cathode type , the cathode (N side) of all LEDs are tied together to a single terminal which is usually labeled as ‘com‘ and the anode (P side) of all LEDs are left alone as individual pins labeled as a, b, c, d, e, f, g & h (or dot) .
In common anode type, the anode of all LEDs are tied together as a single terminal and cathodes are left alone as individual pins.

## Slide 14: Interfacing 7 segment display
330
PA.7
LED ‘dp’
330
LED ‘a’
+5V
GND
g
f
e
d
c
b
PA.0
Common Cathode

## Slide 15: 7-Segment Display
dp | g | f | e | d | c | b | a | Hex | dig
0 | 0 | 1 | 1 | 1 | 1 | 1 | 1 | 3F | 0
0 | 0 | 0 | 0 | 0 | 1 | 1 | 0 | 06 | 1
0 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 5B | 2
0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 4F | 3
0 | 1 | 1 | 0 | 0 | 1 | 1 | 0 | 66 | 4
0 | 1 | 1 | 0 | 1 | 1 | 0 | 1 | 6D | 5
0 | 1 | 1 | 1 | 1 | 1 | 0 | 1 | 7D | 6
0 | 0 | 0 | 0 | 0 | 1 | 1 | 1 | 07 | 7
0 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 7F | 8
0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 6F | 9
a
b
d
c
f
dp
e
g
0 1 2 3 4 5 6 7 8 9

## Slide 16: C Code for Outputting Data
#include <mega32.h>
#include <delay.h>
int digit_cathode[10]={0x3F,0x06,0x5B,0x4F,0x66,0x6D,0x7D,0x07,0x7F,0x6F};
int i;
void main(void) {
DDRB=0xFF;
while (1)
{
for (i=0; i<10; i++)
{
PORTB=digit_cathode[i];
delay_ms(1000);
}
}
}

## Slide 17: Multiple 7-Segment Display
Suppose you need a four digit display connected to the AVR ATmega32.
Each 7 segment display have 8 pins and so a total amount of 32 pins are to the connected to the microcontroller and there will be no pin left with the microcontroller for other input output applications.
More over four displays will be ON always and this consumes a considerable amount of power.
All these problems associated with the straight forward method can be solved by multiplexing .

## Slide 18: Multiplexing 7-Segment Display
In multiplexing all displays are connected in parallel to one port and only one display is allowed to turn ON at a time, for a short period.
This cycle is repeated for at a fast rate and due to the persistence of vision of human eye, all digits seems to glow.
The main advantages of this method are
  Fewer number of port pins are required .
  Consumes less power.
  More number of display units can be interfaced.
The circuit diagram for multiplexing 2 seven segment displays to the AVR ATmega32 is shown in the next slide.

## Slide 19: Connection Diagram of Multiple 7-segment Display with AVR ATmega32
a
b
c
d
e
f
g
dp
PC.0
PC.1
PC.2
PC.3
PC.4
PC.5
PC.6
PC.7
PD.1
ATmega 32
Digit 2
a
b
c
d
e
f
g
dp
Digit 1
LEDs are Common Cathode type
PD.0

## Slide 20: How it works
Let us see how ‘16’ will be displayed in 2 digit display.
Initially the first display is only activated by making PD.0 low and PD.1 high. Then digit drive pattern for “1″ is loaded to the Port C.
This condition is maintained for around 20ms and then PD.0 is made high and PD.1 low.
Then the digit drive pattern for “6″ is loaded to the port C. This will make the second display to show “6″. This condition is maintained for another 20ms.
This cycle is repeated and due to the persistence of vision you will feel it as “16″.

## Slide 21: C Code for 2 digit 7-segment Display
#include <mega32.h>
#include <delay.h>
int digit_cathode[10]={0x3F,0x06,0x5B,0x4F,0x66,0x6D,0x7D,0x07,0x7F,0x6F};
int x=0, y=0, i=0, j=0;
void main(void)
{
DDRC=0xFF;
DDRD=0x03;
while (1)
{
for (i=1; i<100; i++)
{
}
}
}
x=i%10;
y=i/10;
for (j=1; j<20; j++)
{
PORTD=0x01;
PORTC=digit_cathode[x];
delay_ms(20);
PORTD=0x02;
PORTC=digit_cathode[y];
delay_ms(20);
}

## Slide 22: Thanks