## Slide 1
Lecture 4
Pullup Resistors and Interrupts in ATmega32 Microcontroller
S.M. Lutful Kabir
Professor, IICT, BUET
April 2018 ICT 5307 : Embedded System Design

## Slide 2: Role of Pull up resistors at the port pins
Let us say you have configured a port pin as input pin.
If there is nothing connected with the pin and your program reads the state of the pin, will it be high of low? It will be difficult to tell.
This state of the pin is referred to as floating state.
In order to prevent this unknown state, pull up resistor is used.
Pull ups are often used with button and switches.
A switch connected at the input pin without pull up resistor
A switch connected at the input pin with pull up resistor

## Slide 3: Internal pull up resistor in AVR and its control
In AVR ATmega32 microcontroller, each of the port pins have a pull up resistor having the facility of connecting or disconnecting it with the pin.
The provision of connection or disconnection is controlled by PORTx register. [see the figure]
If we put 1s into bits of PORTx register, the pull up resistors are activated.
Remember that during output of data PORTx is the register in which data has to be written to make it out.

## Slide 4: What is an Interrupt?
Interrupt is a method of giving attention to a task which is not scheduled as an usual task
In microcontroller usual task is to follow line by line execution of program.
If a programmer wants to break the flow and attend a different task , then that has to be done by Interrupt.
Whenever such a situation occurs, microcontroller raises a flag corresponding to that task
Programmer can monitor the flag and when he finds the flag raised, he does the specific task - POLLING
OR the programmer set microcontroller in such a way that microcontroller on its own monitor the flag does the task automatically – using ISR

## Slide 5: How Interrupt is handled with the help of an ISR?
Interrupts are basically events that require immediate attention by the microcontroller.
When an interrupt event occurs the microcontroller pause its current task and attend to the interrupt by executing an Interrupt Service Routine (ISR).
At the end of the ISR the microcontroller returns to the task it had paused and continue its normal operations.

## Slide 6: Interrupt Service Routine (ISR)
An Interrupt Service Routine (ISR) or Interrupt Handler is a piece of code that is executed when an interrupt is triggered.
Usually each enabled interrupt has its own ISR.
ISR is also called Interrupt Handler.

## Slide 7: Interrupt Flags and Enabled bits
Each interrupt is associated with two (2) bits, an Interrupt Flag Bit and an Interrupt Enabled Bit. These bits are located in the I/O registers associated with the specific interrupt.
The interrupt flag bit is set whenever the interrupt event occurs, whether or not the interrupt is enabled.
The interrupt enabled bit is used to enable or disable a specific interrupt. Basically it tells the microcontroller whether or not it should respond to the interrupt if it is triggered.

## Slide 8: Both bits should be high
In summary basically both the Interrupt Flag and the Interrupt Enabled are required for an interrupt service routine to be executed as shown in the figure below.
Interrupt Enable
Interrupt Flag
Interrupt Service
Global Interrupt Enable

## Slide 9: Global Interrupt and Enable Bit
Apart from the enabled bits for the specific interrupts the global interrupt enabled bit MUST be enabled for interrupts to be activated in the microcontoller.
For the AVR 8-bits microcontroller this bit is located in the Status I/O Register (SREG).
Upon RESET all interrupts are disabled (masked).
It means that none will be responded by the microcontroller if they occur.
So, the interrupts must be enabled by software in order for the microcontroller to respond to them.
Status Register, SREG
I
T
H
S
V
N
Z
C
D7
D6
D5
D4
D3
D2
D1
D0

## Slide 10: Internal and External Interrupt Sources
The AVR 8-bits microcontroller provide both internal and external interrupt sources. The internal interrupts are associated with the microcontroller's peripherals.
They are the Timer/Counter, Analog Comparator, etc.
The external interrupts are triggered via external pins.
On AVR ATmega32 microcontroller there are four (4) external interrupts:
RESET Interrupt - Triggered from pin 9.
External Interrupt 0 (INT0) - Triggered from pin 16.
External Interrupt 1 (INT1) - Triggered from pin 17.
External Interrupt 2 (INT2) - Triggered from pin 3.

## Slide 11: External Interrupt Pins

## Slide 12: External Interrupts
The number of external hardware interrupts varies in different AVRs.
The ATmega32 has three external interrupts: pin PD2 (PORTD.2), PD3 (PORTD.3) and PB2 (PORTB.2), designated as INT0, INT1 and INT2 respectively.

## Slide 13: External Interrupts INT0, INT1 and INT2
The hardware interrupts must be enabled before they can take effect.
This is done using INTx bit located in GICR (General Interrupt Control Register).
INT1 | INT0 | INT2 | - | - | - | IVSEL | IVCE
GICR Register

## Slide 14: Interrupt Sense Control bits for INT0
SE | SM1 | SM2 | SM0 | ISC11 | ISC10 | ISC01 | ISC00
MCUCR (MCU Control Register)
ISC01 and ISC00 - These bits define the level or edge on the external INT0 pin that activates the interrupts, as shown in the following table
ISC01 | ISC00 |  | Description
0 | 0 |  | The low level of INT0 generates an interrupt request
0 | 1 |  | Change on INT0 generates an interrupt request
1 | 0 |  | Falling edge of INT0 generates an interrupt request
1 | 1 |  | Rising edge of INT0 generates an interrupt request

## Slide 15: Interrupt Sense Control bits for INT1
SE | SM1 | SM2 | SM0 | ISC11 | ISC10 | ISC01 | ISC00
MCUCR (MCU Control Register)
ISC01 and ISC00 - These bits define the level or edge on the external INT0 pin that activates the interrupts, as shown in the following table
ISC11 | ISC10 |  | Description
0 | 0 |  | The low level of INT0 generates an interrupt request
0 | 1 |  | Change on INT0 generates an interrupt request
1 | 0 |  | Falling edge of INT0 generates an interrupt request
1 | 1 |  | Rising edge of INT0 generates an interrupt request

## Slide 16: Interrupt Sense Control bit for INT2
Interrupt 2 (INT2) can only be configures as edge triggered mode.
In other words it can not be configured as level triggered.
ISC2 bit of MCUCSR (MCU Control and Status Register) defines whether INT2 interrupt will activate on falling or rising edge.
IS2 |  | Description
0 |  | Falling edge of INT2 generates an interrupt request
1 |  | Rising edge of INT2 generates an interrupt request
JTD | ISC2 | - | JTRF | WDRF | BORF | EXTRF | PORF
MCUCSR Register

## Slide 17: Sampling the edge-triggered and level-triggered interrupts
The edge-interrupt (the falling edge, the rising edge or the change level) is latched by the AVR.
It is latched by the INTFx bits of GIFR (General Interrupt Flag Register).
This means that when an external interrupt is in an edge-triggered mode (falling edge, rising edge or level change), upon triggering an interrupt request, the related INTFx flag becomes set.
INTF1 | INTF0 | INTF2 | - | - | - | - | -
GIFR Register

## Slide 18: Experiment with Int0
A push button switch is connected in INT0 (PD.2) pin of the ATmega32 microcontroller.
Eight numbers of LEDs are connected in Port C.
One 7-segement display is connected in Port B.
Normally the LEDs will be ON and OFF in every one second.
If push button is pressed the ON-OFF task is hold up and the digits 0-9 will be displayed on the display and
The ON-OFF task is resumed.

## Slide 19: Experiment with Int0 (continued)
The INT0 bit in the GICR register has to be set (i.e. INT0 will be enabled.
At first, we set falling edge as Interrupt sense control.
We have to write an ISR which will be executed only when a falling edge (from 1 to 0) is generated at INT0 pin.

## Slide 20: The Code for Polling Method
#include <mega32.h>
#include <delay.h>
unsigned int cathode[10]={0x3F,0x06,0x5B,0x4F,0x66,0x6D,0x7D,0x07,0x7F,0x6F};
unsigned int i=0;
// A function to display 0-9 in 7-segment display
void seven_seg(void)
{
for (i=0;i<10;i++)
{
PORTB=cathode[i];
delay_ms(1000);
}
GIFR |= 0x40;
}
void main(void)
{
DDRB=0xFF;
DDRC=0xFF;
GICR=(0<<INT1) | (1<<INT0) | (0<<INT2);
MCUCR=(0<<ISC11) | (0<<ISC10) | (1<<ISC01) | (0<<ISC00);
PORTC=0x00;
while (1)
{
if (GIFR & 0x40)
seven_seg();
PORTB=0x00;
PORTC=~PORTC;
delay_ms(1000);
}
}

## Slide 21: The Code Using Interrupt
#include <mega32.h>
#include <delay.h>
unsigned int cathode[10]={0x3F,0x06,0x5B,0x4F,0x66,0x6D,0x7D,0x07,0x7F,0x6F};
unsigned int i=0;
// External Interrupt 0 service routine
interrupt [EXT_INT0] void ext_int0_isr(void)
{
for (i=0;i<10;i++)
{
PORTB=cathode[i];
delay_ms(1000);
}
}
void main(void)
{
DDRB=0xFF;
DDRC=0xFF;
GICR=(0<<INT1) | (1<<INT0) | (0<<INT2);
MCUCR=(0<<ISC11) | (0<<ISC10) | (1<<ISC01) | (0<<ISC00);
#asm("sei")
PORTC=0x00;
while (1)
{
PORTB=0x00;
PORTC=~PORTC;
delay_ms(1000);
}
}

## Slide 22: Interrupt within an Interrupt
When AVR is executing an ISR corresponding to an interrupt, what happens if another interrupt is activated?
In fact, when the AVR begins to execute an ISR, microcontroller, on its own, disables the ‘I’ bit of the SREG register.
So, no other interrupts occur while serving that ISR.
When ISR is finished, the microcontroller again, on its own, enables the ‘I’ bit, causing other interrupts to be served.

## Slide 23: Interrupt within an Interrupt…..
If you want another interrupt (with any priority) to be served while the current interrupt is being served you can set the ‘I’ bit using SEI instruction.
But do it with care.
For example, in a low level triggered external interrupt, enabling the ‘I’ bit while the pin is still active will cause the ISR to be reentered infinitely, causing unpredictable consequence.

## Slide 24: Experiment Demonstrating Multiple Interrupts
Let us say we have two tasks to do.
Task #1 - to display 0-9 digits one by one in a 7-segment display with a delay of 1 sec.
Task #2 - to glow one LED within a group of eight LEDs. Only the leftmost LED will glow first. After one second, only its adjacent one and so on until it reaches to the right most one.
Task #1 will be executed with the interrupt Int0 and Task #2 with Int1.
In the main program both the 7-segment display and the LED group will be made OFF.

## Slide 25: Observation in the Experiment
1. What happens if we interrupt Int0 when Int1 is being executed and vice versa.
2. If you enable Global Interrupt Bit only in the ISR for Int0 what happens if you interrupt Int1 while ISR for Int0 is being served and vice versa.
3. Observe the outcome by enabling Global Interrupt Bit in ISR for Int1 only.
4. Observe the outcome by enabling Global Interrupt Bit in both the ISRs.

## Slide 26: Header file and Variable declaration
#include <mega32.h>
#include <delay.h>
unsigned int cathode[10] = {0x3F,0x06,0x5B,0x4F,0x66,0x6D,0x7D,0x07,0x7F,0x6F};
unsigned int i=0, k=0;

## Slide 27: Main Program multi_int
void main(void)
{
GICR=(1<<INT1) | (1<<INT0) | (0<<INT2);
MCUCR=(1<<ISC11) | (0<<ISC10) | (1<<ISC01) | (0<<ISC00);
MCUCSR=(0<<ISC2);
DDRB=0xFF;
DDRC=0xFF;
#asm("sei")
while (1)
{
PORTB=0x00;
PORTC=0x00;
}
}

## Slide 28: ISR for Int0
// External Interrupt 0 service routine
interrupt [EXT_INT0] void ext_int0_isr(void)
{
// #asm("sei")
for (i=0; i<10; i++)
{
PORTB=cathode[i];
delay_ms(1000);
}
}

## Slide 29: ISR for INT1
// External Interrupt 1 service routine
interrupt [EXT_INT1] void ext_int1_isr(void)
{
// #asm("sei")
PORTC=0x80;
delay_ms(1000);
for (k=1; k<8; k++)
{
PORTC=PORTC>>1;
delay_ms(1000);
}
}

## Slide 30
Thanks