## Slide 1
Lecture 6
ADC Programming
S.M. Lutful Kabir
IICT, BUET
April 2018
ICT5307: Embedded System Design

## Slide 2: ADC Devices
Temperature, pressure, humidity, velocity are a few examples of physical quantities we deal with every day.
A physical quantity is converted into electrical (voltage or current) signals by devices which are called transducer
Transducers are also referred to as sensors.
Most of the sensors produce an output that is voltage (or current)
Therefore, we need an Analogue-to-Digital (ADC) converter to translate analogue signals to digital numbers so that microcontroller can read and process them.

## Slide 3: Block Diagram of an ADC
Vin
Start Conversion
D0
Digital Output
D7
Vref
GND

## Slide 4: Resolution
The ADC has n-bit resolution where n can be 8,10,12,16, or even 24.
Higher resolution ADCs provide a smaller step size, where step size is the smallest change that can be distinguished by the ADC.
We can not change the resolution (number of step) of an ADC but we can control the step size by modifying Vref.

## Slide 5: Reference Voltage, Vref
Vref is the input voltage used for the reference voltage.
The step size (the width of the smallest voltage to be recognized) is determined by this Vref and resolution of the ADC (no. of bits).
For an 8-bit ADC, the step size is Vref/28 or Vref/256.
With a 8-bit ADC, if Vref is equal to 2.56V, then the step size will be 2.56V/256, or 10mV.
In some ADC, differential voltage is required for Vref. In that Vref=Vref(+) – Vref(-).

## Slide 6: Digital Data Output
In 8-bit ADC, the output is D0-D7, whereas for 10-bit ADC, it is D0-D9.
The digital output is given by, Dout=Vin/step size
For example, for Vref=2.56V and 8-bit ADC, if Vin=2.0V, the digital output in decimal is 2.0V/10mV=200D or 11001000b
Find the binary output for the above case, if it was a 10-bit ADC and Vref=5V?
Ans=0110011001b = 1.9971V ?

## Slide 7: Analogue Input Channels
Many data acquisition applications require more than one ADC.
For that reason we see ADC chips with 2, 4, 8 or even 16 channels on a single chip.
The channels are multiplexed.

## Slide 8: Start of Conversion and End of Conversion signals
Since there are multiple input channel and one single output channel, there is a need for a Start of conversion (SC) and End of Conversion (EOC) signals.
When SC is activated, the ADC starts converting the input value of Vin to an n-bit binary number.
When the data conversion is complete, the end of conversion signal notifies the CPU that the converted data is ready for pick up.

## Slide 9: Features of ATmega32 ADC
The ADC peripheral of ATmega32 has the following characteristics
10-bit ADC
8 analogue input channels, 7 differential input channel and two input channel with optional gain of 10x and 200x.
Converted binary data is stored in ADCL and ADCH
ADCH:ADCL makes 16-bit register, but since 10-bit data is saved. 6-bit remains unused.
We have the option of keeping upper 6-bit or lower 6-bit of ADCH:ADCL register unused.

## Slide 10: Features of ATmega32 ADC
We have three option for Vref.
Vref can be connected to AVCC (Analog VCC) or internal 2.56V reference or to external AREF.
The conversion time is dictated by the crystal frequency connected to XTAL pins (Fosc) and ADPS0:2 bits.
NOTE: The AVCC and Vref should be constant. If they vary, the accuracy of ADC conversion is affected.

## Slide 11: ADC programming in AVR
In AVR five registers are used for AVR programming
  ADCH (ADC data register high)
  ADCL (ADC data register low)
  ADCSRA (ADC Control and Status and Register A)
  ADCMUX (ADC Mutliplexer)
  SPIOR (Special Function I/O register)

## Slide 12: ADMUX Register
REFS1:0 – Bit 7:6 – Reference Selection bits
This bits select reference voltage for the ADC. 00- AREF pin, 01- AVCC pin and 10- Reserved and 11- Internal 2.56V
ADLAR – Bit 5 – ADC Left adjust result
1- left adjusted and 0- for right adjusted result
MUX 4:0 – Bit 4:0 – Analogue Channel and Gain Selection bits
Selects the gain of differential channels and selects which combination of inputs are connected to the ADC
REFS0
REFS1
ADLAR
MUX4
MUX3
MUX2
MUX1
MUX0

## Slide 13: ADMUX Register
Either single ended or differential input can be selected for conversion.
If you select single ended input, you can choose the input channel among ADC0 – ADC7. Table shows the MUX4:0 inputs for different single ended selection
MUX4:0 | ADC Channel
00000 | ADC0
00001 | ADC1
00010 | ADC2
00011 | ADC3
00100 | ADC4
00101 | ADC5
00110 | ADC6
00111 | ADC7

## Slide 14: ADMUX Register
For differential inputs the MUX4:0 bits are shown in the table
The Table shows that you can select the positive input to be one of the pins ADC0 to ADC7 and negative input to be ADC0, ADC1 or ADC2
MUX4:0 | Dif(+) | Diff(-) | Gain
01001 | ADC1 | ADC0 | 10X
01011 | ADC1 | ADC0 | 200X
01101 | ADC3 | ADC2 | 10X
01111 | ADC3 | ADC2 | 200X
10000 | ADC0 | ADC1 | 1X
10010 | ADC2 | ADC1 | 1X
10011 | ADC3 | ADC1 | 1X
10100 | ADC4 | ADC1 | 1X
10101 | ADC5 | ADC1 | 1X
10110 | ADC6 | ADC1 | 1X
10111 | ADC7 | ADC1 | 1X
11000 | ADC0 | ADC2 | 1X
11001 | ADC1 | ADC2 | 1X
11011 | ADC3 | ADC2 | 1X
11100 | ADC4 | ADC2 | 1X
11101 | ADC5 | ADC2 | 1X

## Slide 15: ADLAR bit operation
ADLAR=1
Left Justified
ADLAR=0
Right Justified
D9
D8
D7
D6
D5
D4
D3
D2
D1
D0
UNUSED
D9
D8
UNUSED
D7
D6
D5
D4
D3
D2
D1
D0

## Slide 16: ADCSRA Register
ADEN – Bit 7 – ADC Enable
ADSC – Bit 6 – ADC start conversion
ADATE – Bit 5 – ADC auto triggered enable
ADIF – Bit 4 – ADC Interrupt flag
This bit is set when ADC conversion completes and the data registers are updated
ADIE – Bit 3 – ADC Interrupt Enable
ADPS2:ADPS0 – Bit 2:1 – ADC Prescaler Select bits
These bits determine the division factor between the XTAL frequency and the input clock to the ADC.
ADSC
ADEN
ADATE
ADIF
ADIE
ADPS2
ADPS1
ADPS0

## Slide 17: ADC Start Conversion bit
ADSC – by setting this bit conversion of ADC starts. ADC has a special circuit to trigger start conversion
Apart from this bit there are option to select Auto triggering mode by setting ADATE bit
Auto triggering mode or manual triggering can be understood by the block diagram shown in the next slide.

## Slide 18: ADC Conversion Time
By using ADPS2:0 bits we can set the ADC conversion time.
To select conversion time we can select any of Fosc/2, Fosc/4, Fosc/8, Fsoc/16, Fosc/32, Fosc/64 or Fosc/128 for ADC clock, where Fosc is the frequency of the crystal connected to AVR chip
For AVR, the ADC requires an input clock frequency less than 200 kHz for maxm accuracy

## Slide 19: AVR ADC Clock Selection
ADPS0
ADPS1
ADPS2
7-bit prescaler
1
2
3
4
5
6
7
ADC CLOCK SOURCE
ADPS2 | ADPS1 | ADPS0 | ADC CLOCK
0 | 0 | 1 | CLK/2
0 | 1 | 0 | CLK/4
0 | 1 | 1 | CLK/8
1 | 0 | 0 | CLK/16
1 | 0 | 1 | CLK/32
1 | 1 | 0 | CLK/64
1 | 1 | 1 | CLK/128

## Slide 20: Steps of Programming
Step #1: Make the pin for the selected ADC channel as Input pin
Step #2: Enable the ADC
Step #3: Select the conversion speed
Step #4: Select voltage reference and ADC input channels
Step #5: Set the Start Conversion bit, ADSC
Step #6: Wait for some time and continuously monitor the ADIF bit.
Step #7: After ADIF bit is found to be high, ADCL and ADCH bytes are read
Step #8: If want to read the selected channel again go to step 5

## Slide 21: An Experiment on ADC
A variable voltage source will be connected to one of the channel of ADC. It is channel ADC0 (1st channel).
The analogue voltage will be converted into digital form by the ADC.
The voltage read and after converting into decimal will be displayed on LCD.
Reference voltage will be connected to AVCC.
ADC frequency to be chosen to CLK/128. So, for 16 MHz crystal, ADC frequency will be 16 MHz/128=125 kHz

## Slide 22: Program (Part-I)
MUX4:0 | ADC Ch.
00000 | ADC0
00001 | ADC1
00010 | ADC2
00011 | ADC3
00100 | ADC4
00101 | ADC5
00110 | ADC6
00111 | ADC7
REFS0
REFS1
ADLAR
MUX4
MUX3
MUX2
MUX1
MUX0
ADMUX
ADSC
ADEN
ADATE
ADIF
ADIE
ADPS2
ADPS1
ADPS0
ADCSRA
#include <mega32.h>
#include <delay.h>
#include <stdlib.h>
#include <alcd.h>
interrupt [ADC_INT] void adc_isr(void)
{
float adc_data;
char disp[16];
// Read the AD conversion result
adc_data=ADCW/204.8;
ftoa(adc_data,2,disp);
lcd_gotoxy(0,0);
lcd_puts(disp);
}

## Slide 23: Program (Part-II)
void main(void)
{
ADMUX=0b01000000;
ADCSRA=(1<<ADEN) | (0<<ADSC) | (0<<ADATE) | (0<<ADIF) | (1<<ADIE) | (1<<ADPS2) | (1<<ADPS1) | (1<<ADPS0);
lcd_init(16);
#asm("sei")
while (1)
{
delay_us(10);
ADCSRA |= (1<<ADSC);
delay_ms(1000);
}
}

## Slide 24: Temperature Sensor
Temperature Sensor IC => LM35
Resolution of the sensor => 0.01 V per 10 C
For 1500C => 1.5V
Therefore let us set AREF at 1.5 V
So the resolution of the ADC will be 1.5/1024=1.465 mV
So the REFS1:0 bits should be set at 00.
  for Vref=AREF, REFS1:0=00
  for Vref=AVCC, REFS1:0=01
  for Vref=internal 2.56V, REFS1:0=11

## Slide 25: Program for Temperature Sensor(Part-1)
#include <mega32.h>
#include <delay.h>
#include <stdlib.h>
#include <alcd.h>
interrupt [ADC_INT] void adc_isr(void)
{
float adc_data;
char disp[16];
// Read the AD conversion result
adc_data=ADCW*1.5/10.24;
ftoa(adc_data,2,disp);
lcd_gotoxy(0,0);
lcd_puts(disp);
}

## Slide 26: Program for Temperature Sensor(Part-2)
void main(void)
{
ADMUX=0b00000000;
ADCSRA=(1<<ADEN) | (0<<ADSC) | (0<<ADATE) | (0<<ADIF) | (1<<ADIE) | (1<<ADPS2) | (1<<ADPS1) | (1<<ADPS0);
lcd_init(16);
#asm("sei")
while (1)
{
delay_us(10);
ADCSRA |= (1<<ADSC);
delay_ms(1000);
}
}

## Slide 27: Thanks