## Slide 1
Lecture 8
Timer 1 and Timer2
S.M. Lutful Kabir
Professor, IICT, BUET
April 2018 ICT5307 : Embedded System Design

## Slide 2: Timer1 Programming
Timer1 is a 16-bit timer and has lots of capabilities.
It is split into two bytes. These are referred to TCNT1L and TCNT1H.
Timer1 has two control registers, namely TCCR1A (8-bit) and TCCR1B (8-bit).
TOV1 flag bit goes high when overflow occurs.
There are two OCR registers, namely OCR1A(16-bit) and OCR1B(16-bit).
There are two separate flags for each of two OCR registers, which acts independently. The figure in the next slide explains how they work.

## Slide 3: Comparisons and Overflow in Timer1
OCR1BH OCR1BL
TCNT1H TCNT1L
OCR1AH OCR1AL
=
OCF1B
OCF1A
=
TOV1
Ref. Reg. B
Ref. Reg. A
Timer Reg.
flag
flag
flag

## Slide 4: TIFR (Timer/Counter) Interrupt Flag Register
TIFR Register
TOV0
OCF0
TOV1
TOV2
OCF2
ICF1
OCF1A
OCF1B
TOV1 Timer1 overflow flag bit;
OCF1B Timer 1 output compare B match flag
OCF1A Timer 1 output compare A match flag
ICF1 Input Capture flag
Timer 1

## Slide 5: TIMSK (Timer/Counter) Interrupt Enable Register
TIMSK Register
TOIE0
OCIE0
TOIE1
TOIE2
OCIE2
TICIE1
OCIE1A
OCIE1B
TOIE1 Timer1 overflow ENABLE bit;
OCIE1B Timer 1 output compare B match ENABLE
OCIE1A Timer 1 output compare A match ENABLE
TICIE1 Input Capture ENABLE
Timer 1

## Slide 6: TCCR1A & TCCR1B (Timer Counter Control Registers)
TCCR1A Register
COM1A1
FOC1A, FOC1B – Related to force compare
ICNC1, ICES1 – Related to Input Capture
COM1A1, COM1A0, COM1B1, COM1B0
– Related to Waveform Generation
WGM13, WGM12, WGM11, WGM10 – Mode Selection
CS12, CS11, CS10 – Clock Selection
COM1A0
COM1B1
COM1B0
FOC1A1
FOC1B1
WGM11B1
WGM10B1
TCCR1B Register
ICNC1
ICES1
-
WGM13
WGM121
CS12
CS11
CS10

## Slide 7: Block Diagram for Timer1
Falling Edge
Rising Edge
CLK/1024
CLK/256
CLK/64
CLK/8
CLK
0
1
2
3
4
5
6
7
1
0
2
CLkI/O
MUX
PRESCALER
EDGE DETECTOR
T1
CS12
CS11
CS10
STOP

## Slide 8: An Exercise
Write a program to toggle only the PORTB.5 bit continuously every second. Use timer 1, Normal mode, and 1:256 prescaler to create the delay. Assume XTAL=8 MHz.
Solution:
Prescaler=1:256  ftimer=(8/256) MHz
Ttimer = 256/8 uS = 32 uS
So, number of clock necessary to make a delay of 1sec is (1s/32uS)=31250
Therefore, the number to be loaded in the timer register is (65535-31250+1)=34286=0x85EE
So, TCNT1L=0xEE and TCNT1H=0x85

## Slide 9: The Program Using Timer1
#include ….
interrupt [TIM1_OVF] void timer1_ovf_isr (void)
{
PORTB.5=~PORTB.5;
TCNT1L=0XEE;
TCNT1H=0X85;
TCCR1A=0x00;
TCCR1B=0x04;
}
void main(void)
{
TCNT1L=0XEE;
TCNT1H=0X85;
TCCR1A=0x00;
TCCR1B=0x04;
TIMSK=0x04;
DDRB.5=1;
while (1) {
}
}

## Slide 10: Timer2
Time2 is very similar to Timer0 as this is also a 8-bit Timer.
The only difference is that Timer2 cannot be used as Counter [i.e. for counting external event].
Rather, it can count the pulses of external clock.
The external clock has to be connected to specific two pins of the microcontroller.
The frequency of the external clock is set as such a value that making real time clock is facilitated.
And the frequency of the crystal has to be 32.768 kHz.

## Slide 11: Registers Related to Timer2
TCNT2 register - the number of pulse Timer2 counts
bit0
bit1
bit2
bit6
bit7
bit5
bit4
bit3
bit7
OCR2 register - the value with which the comparison is made
TOV0
OCF0
TOV1
TOV2
OCF2
ICF1
OCF1A
OCF1B
TIFR registers - all INTERRUPT FLAGS (all Timers)
bit0
bit1
bit2
bit6
bit7
bit5
bit4
bit3
TIMSK register – all INTERRUPT ENABLE BITS (all Timers)
TOIE0
OCIE0
TOIE1
TOIE2
OCIE2
TICIE1
OCIE1A
OCIE1B

## Slide 12: TIFR (Timer/Counter) Interrupt Flag Register
TIFR Register
TOV0
OCF0
TOV1
TOV2
OCF2
ICF1
OCF1A
OCF1B
TOV2 Timer2 flag bit
OCF2 Timer2 output compare flag bit
Timer 2

## Slide 13: TIMSK Register
TOIE0
OCIE0
TOIE1
TOIE2
OCIE2
TICIE1
OCIE1A
OCIE1B
TOIE2 Timer2 Overflow interrupt Enable
OCIE2 Timer2 output compare Interrupt Enable
Timer 2

## Slide 14: Real Time Clock using Timer2
Timer2 can be connected to real time counter. For that, we should connect a crystal of 32.768 kHz to TOSC1 and TOSC2 terminals and set AS2 bit of ASSR register.
Timer2 can NOT be used as counter of external events. Rather all setting of CS22:CS20 (3bits of TCCR2 register) are for internal frequency select. Of course the meaning of some of the combinations have different meaning than that of Timer0.

## Slide 15: Block Diagram for Timer2
CLK/128
CLK/64
CLK/32
CLK/8
CLK
0
1
2
3
4
5
6
7
1
0
2
WGM21
WGM20
CONTROL UNIT
MUX
PRESCALER
CS22
CS21
CS20
TOV2
OCF2
COMPARATOR =
TCNT2
COUNT
UP/ DOWN
CLEAR
OCR2
STOP
CLK/256
CLK/1024
AS2
CLKI/O
CLK
TOSC1
TOSC2
T/C Oscillator

## Slide 16: TOSC1 & TOSC2 Pins

## Slide 17: Timer2 Programming
TCCR2 Register
CS20
CS21
CS22
WGM20
FOC2
COM21
COM20
WGM21
FOC2 – Bit 7 – Force Compare Match. This is a write only bit, writing 1 to it causes to act as if a compare match has occurred.
WGM20, WGM21 – Bit 6 and 3 – Mode Selector
0 0 – Normal
0 1 – CTC (Clear Timer on Compare Match)
1 0 – PWM, Phase Correct
1 1 – Fast PWM

## Slide 18: Timer2 Programming (Contd.)
COM 21:20 – Bit 5 and 4
Compare output mode This mode controls the waveform generator (will be discussed in another lecture)
CS22:20 – Bit 2, 1 and 0 – Timer clock selector
(see the next slide)
TCCR2 Register
CS20
CS21
CS22
WGM20
FOC2
COM21
COM20
WGM21

## Slide 19: TIFR (Timer/Counter) Interrupt Flag Register
TIFR Register
TOV0
OCF0
TOV1
TOV2
OCF2
ICF1
OCF1A
OCF1B
TOV2 Timer2 Overflow flag bit
OCF2 Timer2 output compare flag bit
Timer 2

## Slide 20: ASSR (Asynchronous Status Register)
ASSR Register
TCN2UB
AS2
AS2 – When it is zero, Timer2 is clocked from CLKI/O,
When it is set Timer2 works as RTC
OCR2UB
TCR2UB

## Slide 21: A simulation of a stop watch
Let us develop a stopwatch using Timer2
At the beginning it will display 00.00
When the control button is pressed once, the stopwatch will start
On second press it will stop
On third press it will reset to 00.00
On fourth press it will start again and so on
minutes
seconds
Start/Stop/Reset

## Slide 22: The Circuit for a Stopwatch

## Slide 23: Connection of the Port Pins
0 1 2 3 4 5 6 7
Port A
4 5 6 7
Port D
data bits
7 6 5 4 3 2 1 0
Control Values
0111 – 7 h
1011 – B h
1101 – D h
1110 – E h
digit1
digit2
digit3
digit4
To enable a certain digit you have to send ‘0’ in the corresponding control pin and ‘1’ in other pins
Values for digits
(without decimal)
0 – 3E h
1 – 06 h
2 – 5B h
3 – 4F h
4 – 66 h
5 – 6D h
6 – 7D h
7 – 07 h
8 – 7F h
9 – 6F h
Out
X
data bits
7 6 5 4 3 2 1 0

## Slide 24: Header files and variable declaration
#include <mega32.h>
#include <delay.h>
int second=0;
int minute=0;
int second0=0;
int second1=0;
int minute0=0;
int minute1=0;
Int press=0;
int digit_cathod[10]={0X3F,0x06,0x5B,0x4F,0x66,0x6D,0x7D,0x07,0x7F,0x6F};
int digit_cathod_decimal[10]={0XBF,0x86,0xDB,0xCF,0xE6,0xED,0xFD,0x87,0xFF,0xEF};

## Slide 25: Separation of 2 digits for minute and 2 digits for second
void separated_digits(void)
{
second1=second/10;
second0=second%10;
minute1=minute/10;
minute0=minute%10;
}

## Slide 26: Displaying the separated digits
void display_digits(void)
{
PORTD=0x7F;
PORTA=digit_cathod[second0];
delay_ms(1);
PORTD=0xBF;
PORTA=digit_cathod[second1];
delay_ms(1);
PORTD=0xDF;
PORTA=digit_cathod_decimal[minute0];
delay_ms(1);
PORTD=0xEF;
PORTA=digit_cathod[minute1];
delay_ms(1);
}

## Slide 27: Int0 ISR (for resetting/starting stopwatch)
interrupt [EXT_INT0] void ext_int0_isr(void)
{
press++;
if (press==4)
press=1;
if (press==3)
{
second=0;
minute=0;
separated_digits();
}
}

## Slide 28: Timer2 output compare interrupt service routine
interrupt [TIM2_COMP] void timer2_comp_isr(void)
{
TCNT2=0;
if (press==1)
{
second++;
if (second>59)
{
second=0;
minute++;
if (minute>59)
minute=0;
}
separated_digits();
}
}

## Slide 29: Settings for Timer2
// Timer/Counter 2 initialization
// Clock source: TOSC1 pin
// Clock value: PCK2/1024
// Mode: Normal top=0xFF
// OC2 output: Disconnected
ASSR=1<<AS2;
TCCR2=(0<<PWM2) | (0<<COM21) | (0<<COM20) | (0<<CTC2) | (1<<CS22) | (1<<CS21) | (1<<CS20);
TCNT2=0x00;
OCR2=0x20;
// Timer(s)/Counter(s) Interrupt(s) initialization
TIMSK=(1<<OCIE2) | (0<<TOIE2) | (0<<TICIE1) | (0<<OCIE1A) | (0<<OCIE1B) | (0<<TOIE1) | (0<<OCIE0) | (0<<TOIE0);

## Slide 30: Setting for the Interrupt, Global Interrupt and DDRx decleration
// External Interrupt(s) initialization
// INT0: On
// INT0 Mode: Falling Edge
// INT1: On
// INT1 Mode: Falling Edge
// INT2: On
// INT2 Mode: Falling Edge
GICR|=(0<<INT1) | (1<<INT0) | (0<<INT2);
MCUCR=(0<<ISC11) | (0<<ISC10) | (1<<ISC01) | (0<<ISC00);
MCUCSR=(0<<ISC2);
GIFR=(0<<INTF1) | (1<<INTF0) | (0<<INTF2);
// Global enable interrupts
#asm("sei")
DDRA=0xFF;
DDRD=0xF0;

## Slide 31: The infinite while() loop
while (1)
display_digits();
}

## Slide 32: Thanks